The difference between the old and new version for Water Conservation Certification of Faucets

The new standard:

GB 25501-2010《Minimum allowable values of water efficiency and water efficiency grades for faucets》

The old standard:

CQC3224-2009《Water Conservation Certification Criteria for universal faucets》

CQC3225-2009《Water Conservation Certification Criteria for ceramic cartridge faucets》

CQC3226-2009《Water Conservation Certification Criteria for non-contact faucets》

CQC3227-2009《Water Conservation Certification Criteria for time-extended faucets》

At the same time, adding the new standard:

GB 18145-2003《Ceramic cartridge faucets》

CJ/T 194-2004《Non-contact type water supply apparatus》

QB1334-2004《General technical conditions for water tap》

1.ceramic cartridge faucets

| Test Project | The old standard | The new standard | Whether to do difference test |
| --- | --- | --- | --- |
|  | CQC3225-2009《Water Conservation Certification Criteria for ceramic cartridge faucets》 | GB 25501-2010《Minimum allowable values of water efficiency and water efficiency grades for faucets》 GB 18145-2003《Ceramic cartridge faucets》 |  |
| Flow Uniformity | NO | ≤6.0L/min | Y |
| The Maximum Flow | ≤0.15L/s | ≤7.5L/min, meeting the requirements for the explicit flow of enterprises | Y |

2.non-contact faucets

| Test Project | The old standard | The new standard | Whether to do difference test |
| --- | --- | --- | --- |
|  | CQC3226-2009《Water Conservation Certification Criteria for non-contact faucets》 | GB 25501-2010《Minimum allowable values of water efficiency and water efficiency grades for faucets》 CJ/T 194-2004《Non-contact type water supply apparatus》 |  |
| Flow Uniformity | NO | ≤6.0L/min | Y |
| The Maximum Flow | ≤0.15L/s | ≤7.5L/min, meeting the requirements for the explicit flow of enterprises | Y |

3. General water tap

| Test Project | The old standard | The new standard | Whether to do difference test |
| --- | --- | --- | --- |
|  | CQC3224-2009《Water Conservation Certification Criteria for universal faucets》 | GB 25501-2010《Minimum allowable values of water efficiency and water efficiency grades for faucets》 QB1334-2004《General technical conditions for water tap》 |  |
| Flow Uniformity | NO | ≤6.0L/min | Y |
| The Maximum Flow | ≤0.15L/s | ≤7.5L/min, meeting the requirements for the explicit flow of enterprises | Y |